## Slide 1
IIIT ALLAHABAD • MINOR PROJECT MIDSEM EVALUATION
Bandwidth vs. Time Efficiency: Semantic S2S vs. S2T2S Pipelines
Proving the Fundamental Trade-Off in Neural Speech Communication
FunASR SenseVoice Small • DeepSC Transformer • Kokoro Emotion TTS • SpeechTokenizer
Notes: Welcome the committee. Introduce the research theme: Bandwidth vs Time Efficiency. State that this midsem evaluation directly answers the fundamental trade-off between direct semantic S2S and cascade S2T2S pipelines with empirical data.

## Slide 2
The Motivation: The Bandwidth vs. Latency Paradox
PROBLEM FORMULATION
The Bandwidth Perspective
Text as Ultimate Compression: Converting speech to text strips raw acoustics, dropping bitrate to ~100-150 bps (50x lower than G.711).
Shannon Capacity Limits: Spectrum is crowded. Semantic communication saves critical wireless channel uses.
The Common Premise: If text uses vastly fewer bits, shouldn't S2T2S be the undisputed winner?
The Time Efficiency Perspective
Transmission Delay is Gone: Over 5G or modern links, transmitting 500 bytes takes <3 ms. Network lag is negligible.
The Real Delay: Latency in neural pipelines is dominated by algorithmic buffering and model compute.
Human Interaction Limit: ITU-T G.114 mandates delay <200 ms for natural dialogue. Delays >400 ms break conversational flow.
Notes: Highlight the core paradox: On modern networks, physical byte transmission is instant (<3 ms). However, S2T2S introduces huge delay (5-20 seconds). Contrast the bandwidth mindset with the latency mindset. Mention ITU-T G.114 standard (200 ms conversational limit).

## Slide 3
System Architectures: S2T2S vs. Direct Semantic S2S
ARCHITECTURES
Pipeline B: Cascade S2T2S (Implemented & Trained in Project)
Flow: Audio In ➔ SenseVoice ASR (Text + Emotion/Gender) ➔ DeepSC Encoder ➔ Channel ➔ DeepSC Decoder ➔ Kokoro TTS ➔ Audio Out
Key Trait: Mandatory phrase buffering (1.5s - 25s) before DeepSC can encode words. 3-stage cascaded neural inference.
Pipeline A: Direct Semantic S2S (Streaming Audio Tokenizers)
Flow: Audio In ➔ Streaming Neural Tokenizer (SpeechTokenizer / Mimi) ➔ Token Stream ➔ Channel ➔ Streaming Vocoder ➔ Audio Out
Key Trait: Operates on 20 ms frames. First audio is reconstructed as soon as the first frame arrives (TTFA < 65 ms).
Notes: Walk through both architectures. In S2T2S, explain our trained DeepSC model with 22,234 vocabulary, trained across AWGN, Rayleigh, and Rician channels. In S2S, explain frame-by-frame RVQ neural codecs (SpeechTokenizer, Mimi).

## Slide 4
Theoretical Delay Formulation: Mathematical Roots of Latency
MATHEMATICAL MODEL
Latency(total) = T(buffering) + T(encode) + T(transmission) + T(decode)
1. The Context Bottleneck (Algorithmic)
ASR Clause Lookahead: ASR cannot transcribe token-by-token in real time. It must buffer an entire sentence to resolve phonemes and grammar: T_buf ≈ Audio Duration (1.5s - 25s).
TTS Intonation Context: TTS must wait for the entire sentence to compute prosody before synthesizing sound.
2. The Computational Cascade (Inference)
Cascaded Pipeline: Runs 3 heavy models in series: SenseVoice ASR (300-1,200 ms) + DeepSC Transformer (20-250 ms) + Kokoro TTS (1,500-3,000 ms).
S2S Frame Stream: Runs a single lightweight convolutional encoder (~5 ms/frame) and streaming vocoder (~15 ms/frame).
Notes: Explain the mathematical deconstruction of delay. State why T_transmission is trivial (<3ms). Focus on the two key drivers: The Context Bottleneck (algorithmic lookahead) and the Computational Cascade (sequential inference).

## Slide 5
Experimental Setup & The 2×2 Benchmark Matrix
METHODOLOGY
Evaluated 72 automated experimental trials across 6 standardized audio samples, 3 wireless channels (AWGN, Rayleigh Fading, Rician Fading), and SNR ranging from -5 dB to +20 dB.
Metric Dimension | Pipeline A: S2S (SpeechTokenizer) | Pipeline A: S2S (Kyutai Mimi) | Pipeline B: Cascade S2T2S (DeepSC)
Effective Bitrate | 1,500 bps | 1,100 bps | 622 - 1,077 bps (Winner)
Time-to-First-Audio (TTFA) | 63.0 ms (Winner) | 43.0 ms (Winner) | 11,743.2 ms (11.7s avg)
Algorithmic Lookahead | 20 ms Frame (Winner) | 12.5 ms Frame (Winner) | 1,590 to 24,685 ms (Whole clause)
Streaming Usability | Real-Time Conversational | Real-Time Conversational | Non-interactive / Store & Forward
Notes: Present the experimental design. 6 standardized audio samples, 3 wireless channels, -5 to 20 dB SNR. Explain hardware-level instrumentation with time.perf_counter().

## Slide 6
Empirical Result 1: Bandwidth Efficiency (S2T2S Wins)
DATA RATE (BPS)
Key Empirical Findings on Bandwidth:
Short Speech (<3s): S2T2S requires ~1,127 bps due to DeepSC start/end token symbols and 16-dim representation.
Paragraph Speech (>20s): S2T2S effective bitrate drops to 622 bps -- outperforming SpeechTokenizer (1,500 bps) by 2.4x and Mimi (1,100 bps) by 1.8x.
Text Compression Advantage: Text discards acoustic redundancy (timbre, room reverb), preserving purely linguistic semantics.
Notes: Chart 1: Point to the long-duration paragraph bars. Note that S2T2S drops to 622 bps. Explain text semantic compression advantage.

## Slide 7
Empirical Result 2: Time-to-First-Audio (Semantic S2S Wins)
TIME EFFICIENCY (TTFA)
Key Empirical Findings on Latency:
ITU-T G.114 Standard: Humans perceive delay >200 ms as conversational disruption (amber dotted line).
S2S Real-Time Mastery: SpeechTokenizer reaches 63.0 ms; Kyutai Mimi reaches 43.0 ms -- both well within live conversation limits.
S2T2S Latency Explosion: Short greetings take 5,278 ms; paragraphs take 29,169 ms.
Speedup Factor: Semantic S2S delivers audio 186x to 273x faster than S2T2S!
Notes: Chart 2: The critical contrast. Point out the amber 200ms line. S2S is at 43-63ms. S2T2S is at 5,000-29,000ms. A 186x to 273x latency disparity.

## Slide 8
Root Cause Analysis: Proving the Context Bottleneck
LATENCY DECONSTRUCTION
Deconstruction of a 7.25s Utterance:
Phrase Buffering (Red): 7,248 ms (65.6% of total delay) is spent simply waiting for the speaker to finish.
DeepSC Transmission (Blue): Only 175 ms (1.6%). Physical semantic communication is extremely fast.
TTS Synthesis (Purple): 3,000 ms (27.1%) generating full sentence spectrograms.
The Definitive Proof: Even if computation was instantaneous (T_compute = 0), S2T2S still has >7 seconds of delay.
Notes: Chart 3: Deconstruct the 7.25-second utterance. Phrase buffering is 7,248 ms (65.6%). Prove that even with instantaneous compute, S2T2S still has 7+ seconds of delay.

## Slide 9
Scaling Behavior: TTFA vs. Duration & Throughput (RTF)
SCALING COMPLEXITY
Duration Scaling & RTF Nuance:
Linear Scaling O(N): S2T2S TTFA scales linearly with speech length (TTFA ≈ Duration + 4s).
Constant O(1) Streaming: S2S TTFA is completely flat at 63 ms regardless of audio length.
The RTF Paradox: S2T2S has an RTF of 0.06 to 0.15 (16x faster than real-time batch compute). But high throughput cannot overcome the phrase buffer bottleneck.
Notes: Chart 4: Left panel shows linear O(N) scaling for S2T2S vs flat O(1) for S2S. Right panel shows RTF. S2T2S has low compute RTF (0.06), but buffering prevents streaming.

## Slide 10
The Definitive Proof: The Empirical Pareto Frontier
THE MONEY SLIDE ⭐
Mapping the Operating Regimes:
No Single Winner: Neither pipeline occupies the ideal bottom-left origin (low bitrate + low latency).
Conversational Zone (Green): S2S (43-63 ms, 1,100-1,500 bps). Mandatory for interactive calls and conversational AI.
Bandwidth-Constrained Zone (Blue): S2T2S (622-1,000 bps, 5-29s). Optimal for satellite telemetry, voicemail, and sensor logs.
Notes: Chart 5: THE MONEY SLIDE. Walk through the Pareto Frontier. Explain the two distinct operational zones: Conversational Streaming Zone vs Bandwidth Archival Zone. State the core engineering takeaway.

## Slide 11
Physical-Layer Wireless Robustness: DeepSC Under Fading
CHANNEL FIDELITY
DeepSC Channel Performance:
Tested Fading Channels: AWGN, Rayleigh Fading (multipath), and Rician Fading (line-of-sight).
Graceful Degradation: DeepSC maintains semantic BLEU fidelity even at 0 dB without the cliff-edge drop seen in traditional 16-QAM + LDPC systems.
Equalization: Trained complex channel matrices apply zero-forcing equalization directly in neural embedding space.
Notes: Chart 6: Show DeepSC wireless channel robustness. Explain that our model was trained on Europarl and handles AWGN, Rayleigh fading, and Rician fading without cliff effect.

## Slide 12
Engineering Conclusion & Midsem Defense Summary
CONCLUSION
The Proven Engineering Thesis
The Conclusion: 'Converting speech to text yields up to 2.4x reduction in bandwidth, but incurs a 186x to 273x latency penalty due to phrase buffering and cascading inference.'
Takeaway: Direct Semantic S2S is not optimized for raw compression, but for conversational flow.
Midsem Deliverables: Complete pipeline working, 22k vocab model loaded, 72 benchmark trials, 6 publication figures.
Live Demo & Endsem Roadmap
Interactive Demo Ready: Gradio UI running (run_ui.bat) with mic input, channel fading controls, and live constellation scatter plotting.
Endsem Roadmap 1: Integrate native streaming Mimi/SpeechTokenizer encoder weights directly into DeepSC channel loop.
Endsem Roadmap 2: Hardware-in-the-loop over-the-air validation with SDR (HackRF / USRP).
Endsem Roadmap 3: Acoustic evaluation with PESQ and STOI metrics.
Notes: To conclude: our midsem evaluation has proven the trade-off conclusively. S2T2S achieves superior bandwidth efficiency (622 bps) at the cost of a 186-fold latency penalty. Semantic S2S operates frame-by-frame, delivering first audio in 43-63 ms to preserve real-time conversational flow. Thank the committee and open for Q&A and live demo.